## Slide 1: Compressive Sensing and the Cocktail Party Problem
Andy Huynh and Eli Saracino

## Slide 2: The Cocktail Party Problem
Humans can focus in on one voice with many in the background
Can we do the same thing on paper?

## Slide 3: Problem Motivation
Surveillance
Communications
Neuroimaging
Model
Let S be a set of source signals and X a mixture of these signals determined by A. Given X recover S.

## Slide 4: Interspeech 2006 Data Set
Speech Separation Challenge: recognize speech from a target talker in the presence of other speech.
Signals consisted of six word sentences of the form:
  <command> <color> <preposition> <letter> <number> <adverb>
  “Place white at L 3 now.”
Characteristics:
  Relatively narrow but easily confusable vocabulary
  Makes no demands on higher-level language processing
  Highly varied
    Allows for different combinations: Male/Female voices, Male/Male voices, etc.

## Slide 5: Previous Work: Non-negative Matrix Factorization
Schmidt, Olsson. “Single-channel speech separation using sparse non-negative matrix factorization”
Results were not ideal:
  Around 50-60% word recognition rates
Deep Learning and Hidden Markov Models have since surpassed this method of approaching the Problem.

## Slide 6: Previous Work: Compressed Sensing
Let S be a set of source signals and X a mixture of these signals determined by A. Given X recover S.
Key difference: we now have no external or very little external information besides X
Bao, Ye, Xu, Zhou. “A Compressed Sensing Approach to Blind Separation of Speech Mixture Based on a Two-Layer Sparsity Model”

## Slide 7: Methodology
Computing mixing matrix A
  Assume sources are sparse
  At each time instance, 1 source is nonzero
Time Frequency domain is sparser
Points lie on a line given by columns of A
K-Means to find these representations
Time domain
Transform domain
Xu T, Wang W. IEE Workshop on Statistical Signal Processing

## Slide 8: The Quest for “A” Mixing Matrix
1) Compute STFT
2) Normalize vectors in STFT to move all points onto a semi-circle
3) Choose k=# of sources
4) Run k-means on the transform to find an estimated A
Bao, Ye, Xu, Zhou, IEE Transactions on Audio, Speech, and Language Processing

## Slide 9: Adding the Dictionary
is generally a DCT dictionary, but for this application performs poorly
Train a better by using the K-SVD algorithm
“Semi-blind” source separation:
  Train dictionary on dissimilar voices.
Bao, Ye, Xu, Zhou, IEE Transactions on Audio, Speech, and Language Processing

## Slide 10: Extensions of this Work
1 vs All Decomposition
  Iterative method to obtain desired voice
Try principal component analysis (PCA) to find mixing matrix M
  Largest eigenvalue corresponds to the most prominent voice
  Subtract out largest voice after recovery
  Extend to n-voice overs
Xu T, Wang W. IEE Workshop on Statistical Signal Processing
Time domain
Frequency domain

## Slide 11: Questions?